PRO MAX Remote Control

Specification

The Pro Max™ Remote Control System is manufactured by Rain Master Irrigation Systems, Inc.  The remote control system has the following features and functions:

- Can be used with any manufacturers’ 24 volt controller.

- Small compact transmitter with belt clip.

- Auto-up and auto-down operation.

- Independent control of Master Valve and/or Pump.

- Single or Multi-station on capability.

- Timed station operation selectable from 1 to 60 minutes.

- Control up to 999 individual receivers from a single transmitter.

- Turn a program on or off (when used with RME Sentar, RME Hawk, or Evolution DX2 controllers).

- Small, compact receiver for permanent internal mount.

- Detects (provides an audible alert) and protects against field wiring short circuits.

- Automatic resetting circuit breakers, no fuses required.

- Receiver has built-in safety default to automatically turn station off after 60 minutes.

- Audible transmitter and receiver tones verify proper Pro Max operation at all times.

- High tech power miser circuitry means no more battery recharging required ( no down time).

- Transmitter has a single replaceable lithium battery that can be purchased locally and field replaced, no battery charger needed.

- Audible alarm warns of low power condition.

- All metal construction with shock absorbing bumpers.

- Water and mud resistant.

- Comes with a hard cover carrying case.

- Utilizes three mechanisms to insure reliable, interference communications:

- Electrical Characteristics:

a. Input Power

  - Receiver, 22-32 VAC, 50/60 Hz

  - Universal Adapter, 22-32 VAC, 50/60 Hz

  - Transmitter, 6 volt lithium battery (user replaceable)

b. Output Power

- Receiver/Universal Adapter, 24 VAC, 1.5 Amps maximum total output (36VA), 1 Amp per station or Master Valve/Pump

- Mechanical Characteristics:

a. Pro Max Receiver

  - Dimensions: 6 ¼ inch length x 3 ¼ inch width x 1 1/16 inch height

  - Weight: 11 oz

  - Operating Temperature: 0 to 60 degrees Celsius (32 to 140 Degrees Fahrenheit)

  - Storage Temperature: -20 to 70 degrees Celsius (-4 to 158 Degrees Fahrenheit)

  - Humidity Range: 0 to 90% non-condensing

b. Pro Max Universal Adapter

  - Dimensions: 6 ¼ inch length x 3 ¼ inch width x 1 1/16 inch height

  - Weight: 13 oz

  - Operating Temperature: 0 to 60 degrees Celsius (32 to 140 Degrees Fahrenheit)

  - Storage Temperature: -20 to 70 degrees Celsius (-4 to 158 Degrees Fahrenheit)

  - Humidity Range: 0 to 90% non-condensing

c. Pro Max Transmitter

  - Dimensions: 3 inch length x 1 3/8 inch width x 5 1/2 inch height

  - Weight: 12 oz

  - Operating Temperature: 0 to 60 degrees Celsius (32 to 140 Degrees Fahrenheit)

  - Storage Temperature: -20 to 70 degrees Celsius (-4 to 158 Degrees Fahrenheit)

  - Humidity Range: 0 to 90% non-condensing